PROPER CARE OF YOUR CUTTING TABLE

- Apply Lemon Oil for the first time to your brand new cutting table, and then repeat every 6 months or more often if needed.

- You will need approximately 1 gallon of Lemon Oil for each 10 sections of table

- It is best to do it with 2 people, one on each side of the table

- Pour sufficient amount of oil on top of the table in the first section, and spread it through the whole section with small rags.

- Repeat this procedure for next sections.  As rags become saturated with oil, you will need to pour less oil on the table

- After oil is absorbed into the table, clean the table with dry larger rags.

- Clean off all oil that might have gotten on the spreading machine tracks